General Environment
Parameter: new_sess
Default value: TRUE
Description:
Indicates whether this run is treated as a new N-SDM session.
- If TRUE, all steps will be re-run.
- If FALSE, steps already completed in previous runs (according to the checkpoint files stored in the ./tmp/checkpoints folder) will be skipped.
This option is useful when a previous run failed or for testing parameters without recomputing everything. Manually delete the checkpoints to restart after a specific step.

Parameter: exit_any
Default value: TRUE
Description:
If TRUE, N-SDM will stop immediately on any error.
If FALSE, N-SDM attempts to continue despite errors.
In a context of modelling numerous species FALSE is useful to drop failing species but continue with successful ones. Species list is automatically refined with successful species, along with job array dimensions.

Parameter: w_path
Default value: /work/nsdm
Description:
Path to the working directory where all scripts, data and configuration files are stored.

Parameter: svp_path
Default value: /scratch/nsdm_save
Description:
Path where final outputs are transferred and stored permanently.

Parameter: rsync_exclude
Default value: d1_covsels,d2_models,d6_preds,d12_preds-sce
Description:
Output folders excluded when transferring results to svp_path. Default excludes non-essential files, preserving core outputs. (See ./documentation/OUTPUTS_DETAILS.odt for output folder details.)

Parameter: scr_path
Default value: /scratch/nsdm
Description:
Temporary scratch directory for intermediate computations. Files may be deleted automatically after completion (see clear_scr)

Parameter: clear_scr
Default value: TRUE
Description:
If TRUE, clears the scratch directory before starting. This avoids conflicts from older runs.

Parameter: clear_fst
Default value: FALSE
Description:
If TRUE, deletes .fst files (converted covariates and species from a previous run, which can be time consuming). Forces regeneration of these files.

Parameter: module_r
Default value: r
Description:
Name and version of the R module to be loaded on the cluster.

Parameter: module_others
Default value: empty
Description:
Comma-separated list of additional modules (e.g., software stack and dependencies) required to access R on the cluster. This field is cluster-specific and may include components such as compilers, libraries, or environment stacks that must be loaded before the R module (Example on the ETHZ cluster: stack/2024-06,gcc/12.2.0,gdal,udunits/2.2.28). If left empty, only the R module (module_r) will be loaded.

Parameter: lib_path
Default value: /users/R
Description:
Path to the R libraries. Ensure nsdm2 package and dependencies are installed here.

Parameter: seed
Default value: 12345
Description:
Seed value for reproducibility in R scripts (set.seed)
Species Data
Parameter: n_spe
Default value: 3
Description:
Number of species included in the run. If forced_species list is available, it thins it to the first n_spe rows.

Parameter: n_mx_spe
Default value: 3
Description:
Maximum number of species processed simultaneously. Helps prevent memory or scratch overflow. If n_mx_spe < n_spe, several N-SDM run will be started in a loop fashion.

Parameter: forced_species
Default value: forced.psv
Description:
(Optional) Name of the .psv file stored in ./scripts/settings listing species to be used for the run. Each line must contain one species. See the example file provided on GitHub for template.

Parameter: glo_use_reg
Default value: TRUE
Description:
If TRUE, regional species data stored in ./data/species/reg are also included in the global model. If FALSE they are processed independently.

Parameter: pa_po_reg
Default value: po
Description:
Specifies whether regional species data are presence-only (po) or presence-absence (pa).
If set to po, background points are generated. If set to pa, the function uses the 0 values from the optional pa column in the species dataset as absences.

Parameter: pa_po_glo
Default value: po
Description:
Specifies whether global species data are presence-only (po) or presence-absence (pa).
If set to po, background points are generated. If set to pa, the function uses the 0 values from the optional pa column in the species dataset as absences.

Parameter: min_occ_reg
Default value: 50
Description:
Minimum number of occurrences required for a species at the regional level. Species with < min_occ_reg will be discarded.

Parameter: min_occ_glo
Default value: 50
Description:
Minimum number of occurrences required for a species at the global level. Species with < min_occ_glo will be discarded.

Parameter: disag_reg
Default value: TRUE
Description:
If TRUE, applies spatial and/or temporal disaggregation to regional occurrences to reduce sampling bias.

Parameter: disag_glo
Default value: TRUE
Description:
If TRUE, applies spatial and/or temporal disaggregation to global occurrences to reduce sampling bias.

Parameter: thin_dist_reg
Default value: 200
Description:
If disag_reg. Distance threshold for spatial thinning of regional occurrences (level units, usually meters).

Parameter: thin_time_reg
Default value: 5
Description:
If disag_reg. Minimum temporal distance (in years) between retained presences for regional data.

Parameter: thin_dist_glo
Default value: 0.008333333
Description:
If disag_glo. Distance threshold for thinning in global models, (level units, usually degrees).

Parameter: thin_time_glo
Default value: NULL
Description:
If disag_glo. Temporal thinning for global occurrences. NULL = no thinning applied.

Parameter: back_strat
Default value: random
Description:
If pa_po_reg or pa_po_glo is TRUE. Strategy for generating background points in presence-only data:
- random: uniform random
- random_w: weighted using a group-specific bias raster (e.g., mammals_reg.tif), where pixel values typically range from 0 (never sampled) to 1 (always sampled). The prefix should correspond to the target group specified in the group column of the species data (here, mammals). The suffix should correspond to the target level (here, reg).

Parameter: n_back
Default value: 10000
Description:
If pa_po_reg or pa_po_glo is TRUE. Number of background points to generate.

Covariate Data and Selection
Parameter: expert_table
Default value: expert_table.psv
Description:
(Optional) Name of the .psv file for the pre-filtering table listing allowed covariates for each species group, to be stored in ./scripts/settings. See the example file provided on GitHub for template.

Parameter: cov_observ
Default value: c('reg_transport_tlm3d_dist2road', … )
Description:
List of observational covariates, provided in the form level_category_dataset_variable. These are fixed to constant values during predictions to handle observational biases. Leave it NULL if not relevant.

Parameter: cov_observ_val
Default value: median
Description:
If any cov_observ. Specifies how observational covariate values are fixed:
median, zero, or max.

Parameter: tmatch_glo
Default value: FALSE
Description:
If TRUE, when possible, applies temporal matching between occurrence records and covariate data in global models.

Parameter: tmatch_reg
Default value: TRUE
Description:
If TRUE, when possible, applies temporal matching between occurrence records and covariate data in regional models.

Parameter: tmatch_scheme_glo
Default value: npts
Description:
Scheme for temporal matching (global level):
- npts = nearest previous time slice
- nts = nearest time slice (either direction).

Parameter: tmatch_scheme_reg
Default value: npts
Description:
Scheme for temporal matching (regional level):
- npts = nearest previous time slice
- nts = nearest time slice (either direction).

Parameter: cor_cut
Default value: 0.7
Description:
Threshold for Pearson correlation coefficient used to filter colinear covariates.

Parameter: max_thre
Default value: 12
Description:
Maximum possible number of covariates allowed in a model.

Modelling Algorithms and Validation
Parameter: mod_algo
Default value: c('glm','gam','max','rf','gbm')
Description:
List of algorithms to run. ‘esm’ may also be specified, but independently.

Parameter: param_grid
Default value: param_grid.psv
Description:
Name of the .psv file stored in ./scripts/settings specifying the hyperparameter tuning grid. See the example file provided on GitHub for template.

Parameter: reps
Default value: 5
Description:
Number of cross-validation replicates.

Parameter: use_spatial_stratification
Default value: FALSE
Description:
If TRUE, uses spatial clustering (k-means on coordinates) for building training/testing splits. If FALSE, points are drawn randomly (repeated split sampling).

Parameter: use_random_global
Default value: TRUE
Description:
If use_spatial_stratification is TRUE. If TRUE, points for global splits are still drawn randomly while regional remain spatially stratified.

Parameter: eval_crit
Default value: maxTSS
Description:
Metric used for thresholding predictions for threshold-dependent evaluations. Only maxTSS is supported for now.

Parameter: best_met
Default value: Score
Description:
Metric used to select best models (default Score averages AUC’, Boyce, maxTSS).

ESM-Specific Parameters (Ensemble of Small Models)
Parameter: ncov_esm
Default value: 5
Description:
Maximum total number of covariates to be evaluated in the ESM framework.

Parameter: comb_esm
Default value: 2
Description:
Number of covariates combined in each ESM model.

Parameter: best_thre_esm
Default value: 0.5
Description:
Threshold for retaining ESM models based on performance metric best_met.

Ensembling
Parameter: do_weighting
Default value: FALSE
Description:
If TRUE, individual algorithms are weighted in ensembles based on a chosen metric.

Parameter: weight_metric
Default value: Score
Description:
Metric for weighting and discarding algorithms in ensembles (default Score averages AUC’, Boyce, maxTSS).

Parameter: disc_thre_glo
Default value: -1
Description:
Global model algorithms with score below this threshold are discarded. -1 = keep all.

Parameter: disc_thre_reg
Default value: -1
Description:
Regional model algorithms with score below this threshold are discarded. -1 = keep all.

Nesting
Parameter: n_levels
Default value: 2
Description:
Number of nested modelling levels:
- 1 = Global only
- 2 = Global + Regional

Parameter: nesting_methods
Default value: c('covariate','multiply')
Description:
Methods for nesting global and regional models (covariate and/or multiply nesting).

Parameter: multiply_weighted
Default value: TRUE
Description:
If TRUE, also computes a weighted version of the multiply nested ensemble, using the weight_metric.

Predicting and Projecting
Parameter: mask_pred
Default value: lakes_mask.tif
Description:
Optional binary raster .tif prediction mask (0/1) stored in the folder ./data/masks. Pixels with value 0 are excluded from predictions. See the example file provided on GitHub for template.

Parameter: do_proj
Default value: TRUE
Description:
If TRUE, performs projections under alternative scenarios.

Parameter: proj_scenarios
Default value: c('rcp45','rcp85')
Description:
List of scenario names. Must match names in covariate scenario folders.

Parameter: proj_periods
Default value: c('2085')
Description:
Projection periods, must match names covariate scenario folders.

HPC Ressources
Parameter: pre_A_m
Default value: 75G
Description:
Requested memory (RAM) for the Preprocessing A step. Adjust this value depending on dataset size and cluster constraints.
The same applies to all other steps (pre_B, glo_A, glo_B, glo_C, reg_A, reg_B, reg_C, sce_A, sce_B, sce_C, sce_D).

Parameter: pre_A_t
Default value: 00-00:15
Description:
Maximum wall-clock time requested for the Preprocessing A step. Format is DD-HH:MM. Ensure sufficient runtime to complete computations.
The same applies to all other steps (pre_B, glo_A, glo_B, glo_C, reg_A, reg_B, reg_C, sce_A, sce_B, sce_C, sce_D).

Parameter: pre_A_c
Default value: 10
Description:
Number of CPU cores allocated to the Preprocessing A step.
The same applies to all other steps (pre_B, glo_A, glo_B, glo_C, reg_A, reg_B, reg_C, sce_A, sce_B, sce_C, sce_D).